## Slide 1: ENGI 301 Wearable Metronome Proposal – Project 2
11/26/2019
Hoang Vu

## Slide 2: Background Information
A wearable metronome/sound sensor, functions include:
  Vibrates at a set tempo
  LED patterns according to noise level
  Optional (different mode for different rhythms/scales)
Advantage: replace traditional sound metronome with vibrational indication direct to musicians
  Do not interfere with recording
  Usable in loud noise situation

## Slide 3: Board Functionality
PCB consists of a wearable metronome that vibrates at a set tempo and reacts to surrounding music
Components includes
  PocketBeagle as a central processing unit
  HEX display to display the tempo
  Button to control the tempo
  Vibrational motors
  USB connection to power source
  USB connection to microphone

## Slide 4: System Block Diagram
PocketBeagle
LED + 680 Ohms resistor
Power Bank
Vibrational Motor
4-digit 7-segment Display
USB Port
I2C2
PWM0BPWM1A
PWM2B
GPIO58
Multifunctional Button
3.3V
GND
GPIO117
330 Ohms Resistor
USB1
Microphone
(through microusb breakout board and audio adapter

## Slide 5: Power Block Diagram
5V
3.3V
85 mA
PocketBeagle
LED + 680 Ohms resistor
Power Bank
Vibrational Motor
4-digit 7-segment Display
USB Port
I2C2
PWM0BPWM1A
PWM2B
GPIO58
Multifunctional Button
GND
GPIO117
330 Ohms Resistor
USB1
Microphone
(through microusb breakout board and audio adapter
3.3V
3.3V

## Slide 6: Mechanical Block Diagram
HEK Display
2’’ x 0.75’’
PocketBeagle
2’’ x 1.25’’
Button
LED Connection
Vibrating motors
USB2 Connection
3’’ x 2.5’’ PCB - Front
3’’ x 2.5’’ PCB - Back